## Slide 1: Shelter AND Settlement
Lutheran World Federation

## Slide 2: By the end of this session you will be able to:
Apply Sphere guidance to improve shelter assistance for immediate emergency programming and for the longer term
Visualise some commonly cited Sphere shelter indicators and describe them in “human terms” rather than simply as numbers
Identify strengths and challenges of different shelter programming options in different contexts
Notes: Introduce the learning objectives. Ask if there are any architects, engineers, or shelter experts in the group. If so, ask them to identify themselves and briefly describe their experience in the sector. Ask if they would be comfortable to be called on for their specific perspectives to shelter issues raised in this session. Explain that the Sphere guidance for this sector can be used for all phases of the programme cycle, but that this session design will highlight primarily the strategy development and programme design phase of the cycle.

## Slide 3: What does shelter provide to people in need?
Notes: Ask the question and have participants contribute answers in a quick brainstorm in plenary. Allow about 2 minutes for the group to answer with as many responses as possible. Write key points to the flipchart. You will come back to this in a moment, so keep it handy.

## Slide 4: What shelter provides:
See page 241
Notes: Point out which of these aspects the participants identified in the quick brainstorm exercise and take a moment to highlight any elements that they did not list, taking the time to read the descriptions below each of the headings. Refer participants to the diagram which is taken from page 241 of the Sphere Handbook. The important point is that shelter, like the other technical sectors, is not a stand-alone aspect of humanitarian response; it overlaps and affects all other areas of response, and they in turn affect it.

## Slide 5: Video analysis preparation instructions
Watch the short video that follows and take notes as needed to answer the two questions below.
What are the two overarching goals of the CRS ”rapid response and recovery cycle” described in the video?
What are the key shelter programme principles and priorities mentioned or illustrated in the video?
Notes: Explain that the next part of the session is based on the analysis of a short video prepared by CRS (Catholic Relief Services). It provides an example from the Philippines as well as an overview of its approach to shelter programming globally. Ask participants to write down these questions and take notes while watching the video to answer them afterwards.
Exercise timetable:
Instructions – 4 mins
Video – 6 mins
Debriefing and summary – 10 mins
Total – 20 mins

## Slide 6: A holistic view of shelter programming
Notes: Click on the image on the screen to play the embedded video.
Click “cc” in the video to view subtitles.
YouTube: https://www.youtube.com/watch?v=N53yd-HsGDk
NOTE: Seki Hirano, who appears in this video, is one of the lead chapter authors for the Shelter and Settlement chapter in the 2018 Sphere Handbook.

## Slide 7: Video analysis
What are the two overarching goals of the CRS ”rapid response and recovery cycle” described in the video?
What are the key shelter programme principles and priorities mentioned or illustrated in the video?
Notes: Remind the participants of the questions they are to answer on the slide. Use a flip chart to record their answers and to debrief the questions in plenary. This is based on individual responses from the plenary, not separate group discussions at each table. Ask each question in turn, calling on volunteers to answer. Facilitate a short discussion on each.
Facilitator's answer sheet and discussion tips:
The two overarching goals of the CRS rapid response and recovery cycle were – 1. protecting lives, and 2. rebuilding lives. Note that this can also be seen as 1. immediate life-saving emergency response (also relates to protection), and 2. the longer-term response (also relates to dignity).
Record the answers given by the participants for question 2 on a flip chart. This will likely be a wide-ranging list of concepts, terms, and actual principles and priorities. List each and verify the meaning of the answers where needed. Likely answers will include: “emergency response, reconstruction, community-based, market-based, resettlement, in-kind contribution, technical assistance, resilient, culturally appropriate, safe and durable, integrated”. On the flip chart, record as many of these topics as the participants can provide in about 5 minutes, prompting them with “What else did you see?” Or “what else did they talk about in the video?”
Once all these are listed and briefly clarified, ask the group which of the topics listed fall into which of the two goals above (protecting lives and rebuilding lives). Use two different coloured markers to circle the topics that are more emergency shelter assistance and those that are more toward establishing durable solutions. If participants are unclear of the difference, play the video from minutes 2:50 to 3:10 (stop the video after the words “tools and living supplies”), then identify the topics that are considered the most basic yet vital life-saving care, providing basic protection from the elements.

## Slide 8: In summary…
Timely shelter response can save lives in the initial stages of a crisis.
Appropriate shelter is also necessary to promote health, support family and community life, and provide dignity, security, and access to livelihoods.
Every situation is different – you have to tailor the response based on context. (See the shelter and settlement assessment checklist on pages 274–277.)
CARE/Sam Bolitho
Notes: This slide is a quick summary of what has been covered so far. Note the last point – that all responses should be based on context – means that a thorough assessment must be done in every instance. Direct the participants to refer to the shelter and settlement assessment checklist on pages 274–277.

## Slide 9: The Minimum Standards
The Shelter and Settlement Minimum Standards focus on what must be done (what must be in place), rather than how the assistance should be delivered.
German Red Cross/Sohrab Taheri-Sohi
See pages 238–273
Notes: Explain that the next part of the session is a summary of the Sphere Minimum Standards for shelter and settlement and some of the key indicators, rather than a detailed exploration of each of them. Note that those sections highlighted do not represent the most important or priority areas, but rather those that can be visually illustrated in a clear way for a non-technical audience, and some that you are most likely to see referenced or cited in reports and proposals.

## Slide 10
Overarching considerations
Broad  Detailed
Notes: Review the seven Shelter and Settlement Standards and note that this is the simplest structure of the four technical chapters. It has only seven themes with only one standard for each. Note that you will review some of these, and some of the related key indicators in depth together.
Also note that very often “generalists” walk away from a Sphere training remembering only the quantitative indicators of each sector. Sector specialists will have a greater appreciation of the overarching considerations of elements like security of tenure and environmental sustainability. Take the time to inform participants that the content on the latter two standards can be found on pages 266 and 270 respectively. Read the following so as to highlight their importance:
“Security of tenure means that people can live in their homes without fear of forced eviction, whether in communal settlement situations, informal settlements, host communities or after return.”
“Environmental sustainability addresses responsible programming that meets the needs of the present without compromising the ability of future generations to meet their own needs. Ignoring environmental issues in the short term can compromise recovery, worsen existing problems or cause new ones.”

## Slide 11: Shelter and settlement standard 1: Planning
Shelter and settlement interventions are well planned and coordinated to contribute to the safety and well-being of affected people and promote recovery.
Lutheran World Information
Notes: Note how this Sphere standard supports the principle of “integrated response” raised in the video. Note too how it underscores the two goals of “protecting lives and rebuilding lives”.

## Slide 12: Shelter and settlement standard 2: Location and settlement planning
Shelters and settlements are located in safe and secure areas, offering adequate space and access to essential services and livelihoods.
IFRC/Julien Goldstein
Notes: Read the standard. Ask the participants to reflect on any situations where this standard was not met. What were the consequences? Ask if shortcomings in this standard can be mitigated by compensating in other sectors of the response.

## Slide 13: Key indicators
% of settlement sites that offer enough usable surface area to carry out private and public outdoor activities appropriate to the context:
    45m2 for each person in camp-type settlements, including household plots
30m2 for each person, including household plots, where communal services can be provided outside the planned settlement area
See pages 250 and 254
Notes: Tactile/visualisation activity: (you will need a 30-metre measuring tape or a pre-marked bit of string for this illustration). Ask for five volunteers, ask everyone to stand up and move to the edges of the room. This should be achievable in most training rooms, but if space is constrained you may need to go outdoors to a nearby open area. You will need a working space about 10m x 6m or larger.
Have one volunteer stand in the middle of the open space. Ask the other four volunteers to play four “corner posts”. Use a measuring tape (or pre-measured length of string/rope/twine) to mark off a rectangular area of 45m2 by asking your “corner posts” to hold up the measuring tape at each of the corners (if using a measuring tape the four corners will be at the 0m, 9m, 14m, 23m, and 28m marks on the tape. The person serving as the first “corner post” will be holding the tape at both the 0m mark and the 28m mark). Ask the participant in the middle of the area if they feel that the space is enough for one person living in a camp. Ask the group if this indicator means that each person should have that much land given to them as their plot in the camp, to do with what they please.
Explain that this is a gross planning figure only, and is not applied to individual plots. This number is only used for assessment or request for the overall site area based on the total population. The figure includes space for roads, open areas, spaces between shelters, schools, religious areas, and all other associated services.

## Slide 14: Example: Za‘Atari Refugee camp – Jordan 2017
Notes: As an example, explain that this is the site plan for the Za’Atari refugee camp in Jordan. Note that all of the items listed in the diagram legend are included in the 45m2/person planning figure.
See page 251 (Surface area of planned or self-settled settlements)

## Slide 15: Shelter and settlement standard 3: Living space
People have access to living spaces that are safe and adequate, enabling essential household and livelihoods activities to be undertaken with dignity.
See page 254
Notes: Read the standard. Ask what the word “adequate” means in this standard. Ask what different ways adequacy might be measured in terms of shelter space. Ask if anyone knows any of the indicators for this standard.

## Slide 16: Key indicators
% of the affected population who have adequate living space in and immediately around their shelters to carry out daily activities
Minimum 3.5m2 of living space per person, excluding cooking space, bathing area and sanitation facility
4.5–5.5m2 of living space per person in cold climates or urban settings where internal cooking space and bathing and/or sanitation facilities are included
See page 254
Notes: Tactile activity: Before the session, mark off a square space of 3.5m2 (which is 1.87m x 1.87m) and a rectangle of 17.5m2 (3.5m x 5m). Masking tape works well for this. Ask for the shortest person in the training group to come up to the front of the room, and stand in the prepared 3.5m2 space. Ask them if this is enough covered space for them, in terms of shelter. Ask if they could sleep comfortably in the space and spread their arms without touching another person. Repeat this with the tallest person in the training group. Ask for three more volunteers and have all five participants move into the 17.5m2 space. Ask the same questions as above, then ask what else needs to happen in this space. Then go to the next slide.

## Slide 17: Example – minimum shelter under roof
One tent (3.5m x 5m) Size = 17.5m2
Shelter space per person = 3.5m2 (for an average family size of 5)
5m
3.5m
Storage
Cooking/ Heating
Storage
Notes: Explain that the standard applies to all people – adults and children – and when calculated at the household level, would result in 17.5 m2 for the family inside this tent. Explain that particularly in distribution of emergency shelter, this is rarely worked out on an individual basis, but rather used to estimate approximately the right-sized tent per family. If the average family size is known (five as in the example), tents should be ordered to accommodate the families based on this figure. Since tents cannot be easily cut down or extended, the units of distribution are then tents designed for an average family. For very large families two or more tents might need to be distributed to the household.

## Slide 18: Shelter and settlement standard 5: Technical assistance
People have access to appropriate technical assistance in a timely manner.
Lutheran World Information
Notes: This standard reflects a key point of the Humanitarian Charter – that the primary responders and the people themselves are responsible for their own recovery. Supporting this idea means providing technical assistance to help them do that in safe and efficient ways. See page 28 (Humanitarian Charter) – “2. We acknowledge that it is firstly through their own efforts, and through the support of community and local institutions, that the basic needs of people affected by disaster or conflict are met.”
Take the time to ask if someone in the group can define technical assistance. Note there is not a single definition but many context-specific answers. If none are provided you can use "providing expertise to promote development" or in some cases technical assistance could mean “specifically, providing technical knowledge on safer or more effective building techniques that can make a shelter more durable to withstanding the typical elemental forces of the region.” Refer to the guidance notes on page 264: Professional expertise and Increasing technical capacity if participants would prefer examples from the Handbook.

## Slide 19: Remember the proverb:
“There is nothing more permanent than a temporary solution.”
Lutheran World Information
Notes: Short-term solutions often end up being used for a much longer term than they were initially intended. Constant monitoring, evaluation, and community consultations are vital for a successful humanitarian response as people transition through its phases.

## Slide 20: Displacement often lasts years, sometimes decades
The location of the shelters and settlement sites, as well as the planning of neighbourhoods and communities where shelters are situated, are important in supporting the dignity and the recovery of people affected by crisis.
Lutheran World Information
Notes: This statement (from page 240) is a reminder that temporary solutions often remain for decades – plan accordingly.

## Slide 21: Options, options, options
How many different ways of providing shelter can you list?
Indonesian Red Cross/Marwin
Notes: Note that beyond the phase of response, the type of shelter programming is largely going to depend on where the emergency takes place and the nature of the population it is to address. A shelter programme in an urban environment will be very different from one in a rural environment. A shelter programme for a refugee influx will be very different from a reconstruction programme in the wake of a natural disaster, etc.
Conduct a quick brainstorm of the many different options for shelter response that the participants can think of. There is no need to record these to flip charts, just to get a quick sense of the range of responses possible. The participants will investigate these options more closely in a short exercise that follows.

## Slide 22: Strategy development and programme design
Programme planning involves analysis of a range of response options, such as in-kind provision of goods, cash-based assistance, direct service provision, technical assistance, or a mix of these.
Let’s explore some of the shelter response options to consider and the contextual factors that would indicate using or avoiding each.
Notes: Review and analysis activity in small groups:
Instructions
Step 1: Divide the participants into either four or six small groups (if more than 24 people, use six small groups).
Step 2: Instruct participants to turn to page 282 in their Sphere Handbooks.
Step 3: Hand out the printed copies of the file STP 9 Response Options Activity Sheet.docx (one copy per group).
Step 4: Based on the number of groups, assign each group a range of shelter options to review (four groups will have six options each, or six groups will have four options each). For ease of reference, see the group option table on the participant handout.
Step 5: Inform each group that they will need to designate both a facilitator and a presenter for their group.
Step 6: Ask for a volunteer to read the instructions to the entire training group, and to then begin work immediately.
Total time for the group work is 15 minutes – with a further 15 minutes for the debrief.
Debrief:
Ask each group in turn to present their option including why they chose it. Clarify answers as needed so they are understood by everyone.

## Slide 23: Key messages
• Which assistance option(s) are appropriate depends on context (Assistance options, page 282).
• Shelter programming does not only concern protection from the elements (What shelter provides, page 241).
• Shelter needs change over time.
• Assessment, community engagement and consultation are essential components of any shelter and settlement programme.
Notes: Closing summary:
There is no “one-size-fits-all” solution to shelter programming. Each option has its proper place and best use, as well as shortcomings in other contexts. Remember that while Sphere guidance provides standards, actions, indicators, and advice on what should be achieved, the question of which solution or response strategy to use rests with those on the ground. This decision is based on assessment and input from people affected.

## Slide 24
Notes: Thank everyone for their inputs and close the session.